## Slide 1: How the Internet Works
(in 50 mins)
Nick McKeown
Professor of Electrical Engineering
and Computer Science, Stanford University

## Slide 3
My
Program
Someone else’s
Program

## Slide 4
Data
Data

## Slide 5
Data

## Slide 6
Notes: Let’s see how this image is sent across the Internet from one smartphone to another….

## Slide 8: A more accurate model
Nick McKeown
Gates 344, Stanford University
Stanford, CA 94305-9030
USA
Me
You
From
Address
To
Address

## Slide 9: Multiple packets in pipeline at same time
Nick McKeown
Gates 344, Stanford University
Stanford, CA 94305-9030
USA
Me
You
Nick McKeown
Gates 344, Stanford University
Stanford, CA 94305-9030
USA
Nick McKeown
Gates 344, Stanford University
Stanford, CA 94305-9030
USA
Nick McKeown
Gates 344, Stanford University
Stanford, CA 94305-9030
USA
Nick McKeown
Gates 344, Stanford University
Stanford, CA 94305-9030
USA

## Slide 10: Packets may be damaged
Data
Data
?!%%*

## Slide 11: Packets may arrive out of order
1
2

## Slide 12: Packets may be duplicated
Data
Data
Duplicate

## Slide 13: They may not arrive at all!
Data
Data
Full

## Slide 14: Summary so far
Applications send and receive data in packets….
…over an Internet that is unreliable.

## Slide 15: How packets find their way across the Internet

## Slide 16: Internet addresses
Data
Internet “IP”
Address
Data

## Slide 17: Internet Addresses (“IP address”)
All Internet packets carry a destination IP address.
We usually write the IP address like this:
171.64.74.58
Data
Internet “IP”
Address

## Slide 18: Routers forward packets one at a time.
Data
Data
Routers look at IP addresses, then send packets to a router closer to the destination.

## Slide 19: IP Addresses
The IP address tells a router where to send the packet next.
IP addresses have structure
171.64.74.58
Stanford University
A network in the CS department at Stanford University
The computer yuba.stanford.edu
88.255.96.208
An address at Koç University
An address managed by RIPE (European IP Networks)
The computer www.ku.edu.tr

## Slide 20: Can we see the path our packets take?
Yes!
On your computer, try: “ping yuba.stanford.edu”
and “traceroute yuba.stanford.edu”
(Windows: “tracert yuba.stanford.edu”)
Notes: traceroute –q1 yuba.stanford.edu

## Slide 21: ping
From yuba, it takes about 115ms to reach Japan and back again (“round-trip-time”)

## Slide 22
Stanford
Kyoto

## Slide 23
Stanford
Kyoto
8,637km
RTT = 86ms
Q: So why did my “ping” take 115ms?

## Slide 24: traceroute

## Slide 25: From Stanford to Doshisha University (Kyoto)
nickm@yuba.Stanford.EDU > traceroute –q1 istc.doshisha.ac.jp
traceroute to istc.doshisha.ac.jp (202.23.190.159), 30 hops max, 40 byte packets
1 csmx-west-rtr.SUNet (171.64.74.2) 0.234 ms
2 hpr-svl-rtr-vlan3.SUNet (171.66.255.186) 0.423 ms
3 hpr-svl-hpr2--stan-ge.cenic.net (137.164.27.161) 0.779 ms
4 hpr-lax-hpr3--svl-hpr3-100ge.cenic.net (137.164.25.73) 8.627 ms
5 sinet-1-lo-jmb-702.lsanca.pacificwave.net (207.231.240.135) 8.793 ms
6 tokyo1-GM-ET-8-3-0-100.s5.sinet.ad.jp (150.99.89.242) 108.852 ms
7 kyoto-RM-ET-7-1-0-1151.s5.sinet.ad.jp (150.99.89.184) 114.829 ms
8 doshisha-LAN.gw.sinet.ad.jp (150.99.196.66) 115.249 ms
9 ***

## Slide 26
Stanford
Kyoto
Stanford-LAX: 500km
LAX-Tokyo: 8,800km
Tokyo-Kyoto: 500km
RTT ~= 100ms

## Slide 28: Try traceroute to….
yuba.stanford.edu, www.google.com, www.ntua.gr, …

## Slide 29
nickm @ home on Comcast network $ traceroute -q1 www.ntua.gr
traceroute to www.ntua.gr (147.102.224.101), 64 hops max, 52 byte packets
1 testwifi.here (192.168.86.1) 0.921 ms
2 96.120.91.229 (96.120.91.229) 8.491 ms
3 be-20052-rur02.santaclara.ca.sfba.comcast.net (68.87.196.49) 10.237 ms
4 162.151.78.129 (162.151.78.129) 8.857 ms
5 be-232-rar01.santaclara.ca.sfba.comcast.net (162.151.78.253) 8.941 ms
6 be-3651-cr02.sunnyvale.ca.ibone.comcast.net (68.86.91.73) 9.485 ms
7 be-11083-pe02.529bryant.ca.ibone.comcast.net (68.86.84.14) 10.357 ms
8 50.248.118.238 (50.248.118.238) 9.467 ms
9 be2016.ccr22.sfo01.atlas.cogentco.com (154.54.0.177) 11.134 ms
10 be3110.ccr32.slc01.atlas.cogentco.com (154.54.44.142) 35.123 ms
11 be3038.ccr22.den01.atlas.cogentco.com (154.54.42.98) 35.458 ms
12 be3036.ccr22.mci01.atlas.cogentco.com (154.54.31.90) 53.296 ms
13 be2832.ccr42.ord01.atlas.cogentco.com (154.54.44.170) 58.615 ms
14 be2718.ccr22.cle04.atlas.cogentco.com (154.54.7.130) 65.101 ms
15 be2994.ccr32.yyz02.atlas.cogentco.com (154.54.31.234) 73.458 ms
16 be3260.ccr22.ymq01.atlas.cogentco.com (154.54.42.90) 85.407 ms
17 be3043.ccr22.lpl01.atlas.cogentco.com (154.54.44.165) 150.394 ms
18 be2183.ccr42.ams03.atlas.cogentco.com (154.54.58.70) 156.881 ms
19 be2814.ccr42.fra03.atlas.cogentco.com (130.117.0.142) 162.831 ms
20 be2960.ccr22.muc03.atlas.cogentco.com (154.54.36.254) 169.709 ms
21 be3462.ccr52.vie01.atlas.cogentco.com (154.54.59.181) 173.362 ms
22 149.6.175.250 (149.6.175.250) 173.362 ms
23 ae1.mx1.ath2.gr.geant.net (62.40.98.146) 200.320 ms
24 grnet-ias-grnet-gw.mx1.ath2.gr.geant.net (83.97.88.66) 206.457 ms
25 eier-kolettir-ae.backbone.grnet.gr (62.217.100.63) 208.703 ms
26 ntua-zogr-3.eier.access-link.grnet.gr (62.217.96.169) 201.891 ms
27 *
nickm@yuba.Stanford.EDU > traceroute -q1 www.ntua.gr
traceroute to www.ntua.gr (147.102.224.101), 30 hops max, 40 byte packets
1 csee-west-rtr-vl3874.SUNet (171.64.74.2) 0.289 ms
2 hpr-svl-rtr-vlan2.SUNet (171.64.255.147) 0.637 ms
3 hpr-svl-hpr3--stan-100ge.cenic.net (137.164.27.60) 0.657 ms
4 hpr-lax-hpr3--svl-hpr3-100ge.cenic.net (137.164.25.73) 8.558 ms
5 hpr-i2--lax-hpr3-r-and-e.cenic.net (137.164.26.201) 8.723 ms
6 ae-5.4079.rtsw.wash.net.internet2.edu (162.252.70.158) 68.694 ms
7 internet2-gw.mx1.lon.uk.geant.net (62.40.124.44) 143.377 ms
8 ae6.mx1.lon2.uk.geant.net (62.40.98.37) 144.475 ms
9 ae5.mx1.par.fr.geant.net (62.40.98.179) 151.959 ms
10 ae5.mx1.gen.ch.geant.net (62.40.98.182) 158.004 ms
11 ae4.mx1.mil2.it.geant.net (62.40.98.89) 164.868 ms
12 ae3.mx2.ath.gr.geant.net (62.40.98.151) 187.210 ms
13 grnet-gw.mx2.ath.gr.geant.net (62.40.124.90) 186.227 ms
14 ntua-zogr-3.eier.access-link.grnet.gr (62.217.96.169) 188.246 ms
15 *

## Slide 30: Summary so far
Applications send and receive data in packets….
…over an Internet that is unreliable.
Packets are forwarded hop-by-hop based on the final destination address.

## Slide 31: The Internet cannot be trusted!!
Data
The Internet doesn’t promise to deliver packets in order.
It doesn’t promise to deliver packets quickly, or on time.
It doesn’t even promise to deliver them at all!
It just makes a “best-effort” attempt.

## Slide 32: Sending data reliably over an Internet that is unreliable

## Slide 33: How Network Applications Communicate
My
Program
Someone else’s
Program
The most common method:
  Communication is in both directions – “bidirectional”.
  Communication is reliable (if there is a working path between the two computers).
It’s like an unformatted pipe:
  You push data in at one end, and it pops out correctly at the other end.
  The applications decide how the data is formatted inside the pipe.

## Slide 34: Byte Stream Model
Internet
Setup connection
A
B

## Slide 35: Byte Stream Model
A
B
Stream of bytes
Internet
Stream of bytes

## Slide 36: Byte Stream Model
Internet
Close connection
A
B

## Slide 37: World Wide Web (HTTP)
Internet
Setup connection
www.stanford.edu
Client
Server

## Slide 38: World Wide Web (HTTP)
Internet
www.stanford.edu
GET/HTTP/1.1 index.html
Stream of bytes
HTTP/1.1 200 OK <…contents of index.html…>
Stream of bytes
Client
Server

## Slide 39: World Wide Web (HTTP)
Internet
www.stanford.edu
Client
Server
Close connection

## Slide 40
“IP”
Your Application program
e.g. Chrome, Skype
Data
“IP”
The server
e.g. Google, Facebook
“TCP”
“TCP”
TCP makes sure all
the data is delivered

## Slide 41: TCP’s job
Makes sure all data is delivered correctly.
Delivers data to the application in the right order.
How?
  Add sequence numbers to every packet (so the receiver can check if any are missing, and put them in right order)
  When a packet arrives, send an acknowledgment of receipt or “ACK” back to the sender
  If no acknowledgment is received, resend the data

## Slide 43: http client (e.g. Chrome)
IP
Application
Ethernet
TCP
http request
TCP
(http)
GET index.html
IP
IP address
(TCP)
TCP
(http)
Ethernet
Ethernet “MAC” address
(IP)
Chrome
TCP
(http)
IP
IP address
(TCP)
TCP
(http)
IP
IP address
(TCP)
Ethernet
Ethernet “MAC” address
(IP)
“Deliver to the http server”
“…at this destination”
“…starting with this link”

## Slide 44: Here it goes….
TCP data
(http)
IP data
IP Address
(TCP)
Ethernet data
Ethernet “MAC” address
(IP)

## Slide 45: http server (e.g. www.google.com)
IP
Application
Ethernet
TCP
http request
TCP
(http)
TCP
(http)
IP
IP address (TCP)
TCP
(http)
IP
IP address
(TCP)
Ethernet
Ethernet “MAC” address
(IP)
GET file
“Deliver to the http server”
“Deliver to TCP”
http server

## Slide 46: Summary of what we learned
Applications send and receive data in packets….
…over an Internet that is unreliable.
Packets are forwarded hop-by-hop using the IP destination address.
Our applications use TCP to make sure they are
delivered and put back in the correct order.
My
Program
Someone else’s
Program