## Slide 1: How packets find their way across the Internet
Nick McKeown
Professor of Electrical Engineering
and Computer Science, Stanford University
CS144 Week 5: Routing

## Slide 2: Routers forward IP datagrams one at a time
Data
Data
Routers uses IP address as a key into a forwarding table, then
Sends datagram to a router closer to the destination.

## Slide 3: The Internet forwards datagrams hop-by-hop
IP Address | Next-hop
A | A
B | R2
C | R3
D | R3
A
B
C
D
IP Address | Next-hop
A | R1
B | R4
C | R4
D | R4
IP Address | Next-hop
A | R3
B | B
C | R3
D | R3
R1
R2
R4
R3
Data
B
Notes: In packet switching, there is no dedicated circuit to carry our data. Instead, we send a block of data by adding a header to it, and call it a packet. The header contains the address of where the packet is going, just like an envelope tells the post office where to send a letter.
<click to send packet on link> A packet switched network consists of end-hosts, links, and packet switches. When we send a packet, it is routed hop-by-hop to its destination. Each packet switch lookups the address in the packet header in its local forwarding table.
For example, this packet is addressed to B. When we transmit it, the first router looks up address B in its local table, and sees that switch S2 is the next hop. S2 and S4 do the same thing, and the packet is eventually delivered to B.In the Internet there are several different types of packet switches. Some of them are called routers or gateways, while others are called Ethernet switches. We’ll learn more about each of them later. At this stage you just need to know that they are both types of packet switch, and they forward packets based on the destination address in the header.

## Slide 4: How do the routers know what forwarding table to use?
What techniques can you think of?

## Slide 5: Here are three ways
Flooding: Every router sends arriving packet to every neighbor
Source Routing: End host lists the routers to visit along the way (in each packet)
Distributed Algorithm: Routers talk to each other and construct forwarding tables using a clever algorithm
You are going to figure this out on your own!!!

## Slide 6: Game: Routing Competition

## Slide 7: Task 1

## Slide 8
5
12, 19
Your router
ID
The IDs of your neighbors

## Slide 9
2
3
4
5
6
7
8
1
15
14
13
12
11
10
9
16
18
19
20
21
22
23
24
17
25

## Slide 10: Task 2

## Slide 11: Find the shortest path
2
3
4
5
6
7
8
1
15
14
13
12
11
10
9
16
18
19
20
21
22
23
24
17
25

## Slide 12: Task 3

## Slide 13: In a real network, the routers don’t know what the network looks like. This time, I won’t show you the network.

## Slide 14
5
12, 19
12
19
3
5, 19
5, 12, 3

## Slide 15: Rules
You may not
  Pass your card to anyone else
  Leave your seat
  Write anything down
You may
  Ask nearby friends (in your group) for advice
  Shout to other participants (anything you want!!!)
  Say bad things about Nick
You must: Participate

## Slide 16: Task 3
Find the shortest path from Node 1 to Node 40.
When you are done, you must be able
to repeat it correctly.
The first group to finish is the champion!!

## Slide 17: Pink Group
1
…
…
…
…
…
2
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
3
…
…
…
…
…
…
…
…
…
…
…
…
40

## Slide 18: Go!

## Slide 19: An algorithm to find the shortest path

## Slide 20
1
24
14
27
25
15
9
6
10
32
26
30
12
4
23
22
3
29
31
2
7
28
17
5
19
8
20
13
11
21
18
16
1
1
2
2
2
2
3
3
3
3
5
5
5
5
5
6
6
6
8
8
8
7
7
7
9
9
10
10
10
11
11
12
12
12
4
4
4
4
4
“You can reach node 2 in 1 hop from node 22”
IP Address | Next-hop
Node 2 | Node 4

## Slide 21
1
24
14
27
25
15
9
6
10
32
26
30
12
4
23
22
3
29
31
2
7
28
17
5
19
8
20
13
11
21
18
16
1
1
2
2
2
2
3
3
3
3
4
4
4
4
5
5
5
5
6
5
6
6
7
8
8
8
7
7
9
10
11
9
12
10
12
10
11
12
4
Notes: Q: How do we know there are no loops?
Q: How many steps does it take?
Q:

## Slide 22: What if each link has a “cost”?

## Slide 23
“Expensive link”:
It might be very long. e.g. a link from Europe to USA.
Or it might be very busy. e.g. it connects to Google or CNN.
Or it may be very slow. e.g. 1Mb/s instead of 100Mb/s.
Cost = 4+9 = 13
Cost = 1+4+4+2 = 11
A
B
C
D
E
F
G
H
1
4
4
2
9
4
1
1
5
1
5
2

## Slide 24: Find lowest cost path to H
1
4
4
2
9
4
1
1
5
1
5
2
2
9
5
1
6
2
7
6
14
13
A
B
C
D
E
F
G
H

## Slide 25: Find lowest cost path to H
A
B
C
D
E
F
G
H
1
4
4
2
9
4
1
1
5
1
5
2
2
9
5
1
6
2
7
6
14
13
7
4
11
7
5
6

## Slide 26: Find the lowest cost path
1
24
14
27
25
15
9
6
10
32
26
30
12
4
23
22
3
29
31
2
7
28
17
5
19
8
20
13
11
21
18
16
1
6
1
1
1
1
1
7
1
1
1
2
7
1
1
1
12
3
1
4
3
1
1
10
1
1
8
1
4
11
1
5
6
2
1
1
1
1
1
Router 4 tells its neighbors:
“I can reach 2 with a cost of 15”

## Slide 27: Solution
1
24
14
27
25
15
9
6
10
32
26
30
12
4
23
22
3
29
31
2
7
28
17
5
19
8
20
13
11
21
18
16
1
6
1
1
1
1
1
7
1
1
1
2
7
1
1
1
12
3
1
4
3
1
1
10
1
1
8
1
4
11
1
5
6
2
1
1
1
1
1
Cost = 22
3
1
7
5
16
17
28
7
8
18
2
4
4
15
15
6
17
18
…and so on!
9
11
12
13
14
17